## Slide 1: Colts Circle
Lawrence Township Station 21

## Slide 2: Access divisions 1-2-3 stairways
A-B
A-D
BC
CD

## Slide 3: Access
Complex is Knox Box accessible.
Contact Mercer County Central
The code will be sent via the old VHF system
Access card is for the double lock doors
Access card is needed for basement entry
  Elevator machinery / hydraulic relief valve
  Sprinkler system / wet and dry valves
  Electrical room
  Annunciator panel

## Slide 5: Interior card

## Slide 6: Lobby / apartment call box

## Slide 7: Apartment key storage
Keys from Knox Box

## Slide 8: A-d side (princeton pike)

## Slide 9: A side to d corridor

## Slide 10: A-b side (us1)

## Slide 11: Basement alarm panel

## Slide 12: elevator lift assembly
Needle Valve can be used to lower elevator USE CAUTION

## Slide 13: ELECTRICAL DISCONNECT

## Slide 14: Sprinkler system

## Slide 15: Wet system valve / dry valve

## Slide 16: From fdc / domestic water

## Slide 17: Exposure sides
A
B
C
D

## Slide 18: Grade level access only

## Slide 19: Notes/ access/ utilities
Roof Access is on Division 4 at Bravo side.
HVAC units in the storage areas supply common areas only.
Gas meters are on the A/B corner and B/C corner.
All units have gas stoves.
All units have electric dryers.
The gas heaters for each unit are located on the balcony of each unit.

## Slide 20: Notes / standpipes
All stairways have standpipe connections
All stairways have exterior access.
Hose lays floor to floor from standpipe / require 50’ hose.
From the Bravo and Delta standpipe into the corridor to the center of the corridor requires approximately 133 ‘ of hose.
Typically on 50’ length of hose is needed for interior apartment fire attack.

## Slide 21: Additions / corrections
Please contact Capt. Ken Kandrac 609-883-5435 or bckk1@verizon.net for additions or corrections.